## Slide 1: SAM® Junctional Tourniquet (SJT) Training
sammedical.com

## Slide 2: Force Multiplication With One Device
Recent studies indicate
  Junctional hemorrhage accounts for up to 20% of preventable deaths in combat. Immediate, effective treatment is necessary for patient survival.*
  24% of patients with traumatic lower limb amputations from IEDs had associated pelvic fractures**
*Death on the battlefield (2001-2011): Implications for the future of combat casualty care. J Trauma Acute Care Surgery. Eastridge et al. Volume 73, Number 6, Supplement 5
**British Editorial Society of Bone & Joint Surgery (2010): Lower Limb Traumatic Amputations - The importance of pelvic binding for associated pelvic fractures in blast injury. Cross et.al .J Bone Joint Surg Br 2012 vol. 94-B no. SUPP XXI 4

## Slide 3: Training Overview
SJT Key Elements
Components of the SJT
Instructions for Use
Considerations

## Slide 4: SJT Key Elements
Multiple Indications
  Pelvic Immobilization
  Control Inguinal Hemorrhage
  Control Axilla Hemorrhage
< 25 second application time
Lightweight (1 lb., 1 oz.) (488 g)
Easy to use, 4 step application
FDA 510(k) cleared and CE marked
Step by step instructions printed directly on the device

## Slide 5: Components of the SJT
The SJT is comprised of four basic parts
  Pelvic Belt
  Hand Pump
  (2) Target Compression Devices (TCD) SJT 102
  Auxiliary Strap and TCD Extender

## Slide 6: Pelvic Belt
Modified SAM Sling
Clinically proven to provide the prescribed safe and effective force for pelvic stabilization
Patented buckle design maintains correct base force to eliminate slack. “Click” provides clear feedback to confirm when to secure Velcro for correct application.

## Slide 7: Hand Pump
Removable Hand Pump quickly inflates the Target Compression Device (TCD) to achieve hemorrhage control
Operates much like a blood pressure bulb and is made of PVC

## Slide 8: Target Compression Device (TCD)
Inflates to 3.2” high
Body of TCD is made of Texin – material also used in protective eyewear, golf ball and whitewater raft protective coating products
Base of TCD is Makrolon polycarbonate material, which is also used in bullet-proof glass and combat helmet products
Body and base are welded, not glued

## Slide 9: AUXILIARY STRAP SUPPORT & TCD EXTENDER
Auxiliary Strap Support - 35” x 2” adjustable Nylon Strap with clips on each end utilized to apply the SJT in a harness-style application
TCD Extender – Attached via lanyard to TCD, used to change the shape of the TCD prior to inflation

## Slide 10: Multiple Indications
Pelvic Stabilization
Control Inguinal Hemorrhage
Control Axilla Hemorrhage
sammedical.com

## Slide 11: To Immobilize Pelvic Fractures

## Slide 12: To Immobilize Pelvic Fractures

## Slide 13: To Immobilize Pelvic Fractures

## Slide 14: Inguinal Hemorrhage

## Slide 15: Occlude Femoral Artery

## Slide 16: To Control Inguinal Hemorrhage
Note: The belt may attach on the left or right of the patient, depending on the location of the injury.

## Slide 17: To Control Inguinal Hemorrhage

## Slide 18: To Control Inguinal Hemorrhage

## Slide 19: To Control Inguinal Hemorrhage

## Slide 20: Axilla Hemorrhage

## Slide 21: Axilla Artery

## Slide 22: To Control Axilla Hemorrhage
Maintain tension and secure the strap by pressing it down on the Velcro.

## Slide 23: To Control Axilla Hemorrhage
The Extender allows for more direct pressure on the artery.

## Slide 24: To Control Axilla Hemorrhage

## Slide 25: To Control Axilla Hemorrhage

## Slide 26: To Control Axilla Hemorrhage

## Slide 27: Considerations
The SAM® Junctional Tourniquet is intended to be left on for up to four hours
Remove only at a Definitive Care Facility
Additional inflation of the TCD may be necessary with changes in altitude

## Slide 28: Specifications
NSN 6515 01 618 7475
Pricing for DOD: $292.50
Available through Cardinal and is on Bound Tree's DAPA http://www.boundtreefed.com/